## Slide 1: Chemical sterilization techniques.
- Miss. Tejaswini Shivaji Vagavekar.
Assistant Professor .
Department of Biotechnology (Entire)
Vivekanand College, Kolhapur

## Slide 2: Introduction.
Microorganisms are very much beneficial as well as harmful to the mankind. i.e. They
causing many diseases to man, animals even plants, spoilage and contamination.
Sterilization :
( Latin – Sterilis – unable to produce offspring)
Is the process by which all living cells, viable spores, viruses, viroids are either destroyed or removed from an object or habitat.

## Slide 3: Sterilization by chemical agents.
Control of microorganisms by chemical agents is employed for many situations.
When sterilisation is achieved by a chemical agents, this chemicals is called Sterilant.
Characteristics of an ideal chemical agents :
Must be effective against wide variety of organisms.
Should not be toxic and harmful.
Must be effective in low concentrations.
Must be inexpensive.
Should be active even in presence of organic matter.
Must penetrate through surfaces.
Must have low surface tension.
Must be soluble in water and other solvents.

## Slide 4: Chemicals .
Phenol & Phenolic compounds.
Alcohols.
Halogen compounds.
Heavy metals.
Gaseous agents.
A) Phenol & Phenolic compounds :
Use of phenol was started by Joseph Lister in 1880s during surgical operations.
Acts by denaturing proteins and disruption of cells.
However, they have unpleasant odour & cause skin irritation.
Used for disinfection of urine, sputum, contaminated equipments.

## Slide 5
B) Alcohols :
Most widely used as disinfectants & antiseptics.
Bactericidal, fungicidal but not sporicidal.
Two most popular alcohol germicides are ethanol & isopropanol , usually used in 60 to 80 % conc.
Acts by denaturing proteins & possibly by dissolving membrane lipids
C) Halogen compounds :
A halogen is any of the five elements i.e. Fluorine, Chlorine, Bromine, Iodine & Astatine.
The halogens Iodine & Chlorine are commonly used as antimicrobial agents.
Chlorine:
Used as usually disinfectant for municipal water supplies & swimming pools & is employed in the dairy & food industries.

## Slide 6
May acts by oxidation of cellular materials & may also combines with cell membrane proteins & enzymes.
Is also an excellent disinfectant for individual use because it is effective, inexpensive & easy to employ.
One potential problem is that chlorine reacts with organic compounds to form Carcinogenic trihalo methanes, which must be monitored in drinking water.
ii) Iodine :
Used as an antiseptic.
It oxidises cell constituents & also iodinated cell proteins.
Is an antiseptic but it causes skin irritation.
Some common brands are –
- Wescodyne: for skin. - Betadine : for wounds.

## Slide 7
D) Heavy metals :
Used as germicide.
Includes use of Hg, Ag, Cu.
Acts by combine with proteins, enzymes.
May also precipitate cell proteins, more specifically cytoplasmic proteins that results into damage or death of cell.
Silver nitrate : used in ophthalmic preparations.
Copper : Copper sulphate is used as an algicide in swimming pools and lakes.
Mercury : Mercuric chloride – used in ointments as antiseptic.
-Organic mercury compounds as metaphen, merthiolate are used as skin disinfectants.

## Slide 8
E) Gaseous agents :
Sterilization of some heat sensitive items is done by using gaseous sterilizing agents.
Ethylene oxide :
Used as microbicidal and sporicidal.
Has great penetration power.
Causes alkylation of enzymes and proteins.
Leads to inactivation of enzymes.
II) Betapropiolactone (BPL) :
Rarely used as sterilizing gas.
Low power of penetration.
Slightly irritating i.e. Causes weeping/ tearing.
Is an effective germicide & sporicide.
Mainly used for sterilization of vaccines and Sera.

## Slide 9
III) Formaldehyde :
Germicide & sporicide Fumes of Formaldehyde are noxious, irritating to eyes & tissues.
Low penetration power.
Combines with with proteins and nucleic acid i.e. Inactivation of proteins and nucleic acids.
Leading to death of cell.

## Slide 10
Thank you...